Configure lan-to-lan tunnels between a main office and two remote offices (sometimes called Hub and Spoke).

This guide shows how to configure tunnels between three firewalls. First create one tunnel from firewall A to firewall B and then a second tunnel from firewall A to firewall C. Users behind firewall B should be able to reach resources behind firewall C (and the other way around).

1. Firewall A - Addresses

Go to Objects -> Address book -> InterfaceAddresses.

Edit the following items:

Change lan_ip to 192.168.3.1

Change lannet to 192.168.3.0/24

Change wan1_ip to 192.168.110.5

Change wan1net to 192.168.110.0/24

Go to Objects -> Address book.

Add a new Address Folder called RemoteHosts.

In the new folder, add a new IP address:

Name: fwB-net

IP Address: 192.168.1.0/24

Click Ok

Add a new IP address:

Name: fwB

IP Address: 192.168.110.1

Click Ok

Add a new IP address:

Name: fwC-net

IP Address: 192.168.2.0/24

Click Ok

Add a new IP address:

Name: fwC-remotegw

IP Address: 192.168.110.3

Click Ok

Add a new IP4 Group:

Name: tunnelAB-localnet

Add lannet and fwC-net to the Group members

Click Ok

Add a new IP4 Group:

Name: tunnelAC-localnet

Add lannet and fwB-net to the Group members

Click Ok

2. Firewall A – Pre-shared keys

Go to Objects -> Authentication Objects.

Add a new Pre-Shared Key.

General:

Name: fwABC-psk

Shared Secret:

Select Passphrase and enter a shared secret.

Click Ok.

3. Firewall A – IPsec tunnel interface

Go to Interfaces -> IPsec.

Add a new IPsec Tunnel.

In the General tab:

General:

Name: ipsectunnelAB

Local Network: tunnelAB-localnet

Remote Network: fwB-net

Remote Endpoint: fwB

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

In the Authentication tab:

Authentication:

Enable Pre-Shared Key and select fwABC-psk from the dropdown list.

Click Ok.

Add a new IPsec Tunnel.

In the General tab:

General:

Name: ipsectunnelAC

Local Network: tunnelAC-localnet

Remote Network: fwC-net

Remote Endpoint: fwC

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

In the Authentication tab:

Authentication:

Enable Pre-Shared Key and select fwABC-psk from the dropdown list.

Click Ok.

4. Firewall A – Rules

Go to Rules -> IP Rules.

Create a new IP Rule Folder called lan_to_fwBC.

In the new folder, add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: ipsectunnelAB

Destination Network: fwB-net

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelAC

Source Network: fwC-net

Destination Interface: ipsectunnelAB

Destination Network: fwB-net

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelAB

Source Network: fwB-net

Destination Interface: lan

Destination Network: lannet

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelAB

Source Network: fwB-net

Destination Interface: ipsectunnelAC

Destination Network: fwC-net

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelAC

Source Network: fwC-net

Destination Interface: lan

Destination Network: lannet

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: ipsectunnelAC

Destination Network: fwC-net

Click Ok.

Save and activate the configuration on firewall A.

5. Firewall B - Addresses

Go to Objects -> Address book -> InterfaceAddresses.

Edit the following items:

Change lan_ip to 192.168.1.1

Change lannet to 192.168.1.0/24

Change wan1_ip to 192.168.110.1

Change wan1net to 192.168.110.0/24

Go to Objects -> Address book.

Add a new Address Folder called RemoteHosts.

In the new folder, add a new IP address:

Name: fwA-net

IP Address: 192.168.3.0/24

Click Ok

Add a new IP address:

Name: fwA

IP Address: 192.168.110.5

Click Ok

Add a new IP address:

Name: fwC-net

IP Address: 192.168.2.0/24

Click Ok

Add a new IP4 Group:

Name: fwB-remotenets

Add fwA-net and fwC-net to the Group members

Click Ok

6. Firewall B – Pre-shared keys

Follow the instructions in step 2 to add a pre-shared key called fwABC-psk to firewall B. The passphrase has to be the same as the passphrase on firewall A.

7. Firewall B - IPsec tunnel interface

Go to Interfaces -> IPsec.

Add a new IPsec Tunnel.

In the General tab:

General:

Name: ipsectunnelBA

Local Network: lannet

Remote Network: fwB-remotenets

Remote Endpoint: fwA

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

In the Authentication tab:

Authentication:

Enable Pre-Shared Key and select fwABC-psk from the dropdown list.

Click Ok.

8. Firewall B – Rules

Go to Rules -> IP Rules.

Create a new IP Rule Folder called lan_to_fwA.

In the new folder, add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: ipsectunnelBA

Destination Network: fwB-remotenets

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelBA

Source Network: fwB-remotenets

Destination Interface: lan

Destination Network: lannet

Click Ok.

Save and activate the configuration on firewall B.

9. Firewall C - Addresses

Go to Objects -> Address book -> InterfaceAddresses.

Edit the following items:

Change lan_ip to 192.168.2.1

Change lannet to 192.168.2.0/24

Change wan1_ip to 192.168.110.3

Change wan1net to 192.168.110.0/24

Go to Objects -> Address book.

Add a new Address Folder called RemoteHosts.

In the new folder, add a new IP address:

Name: fwA-net

IP Address: 192.168.3.0/24

Click Ok

Add a new IP address:

Name: fwA

IP Address: 192.168.110.5

Click Ok

Add a new IP address:

Name: fwB-net

IP Address: 192.168.1.0/24

Click Ok

Add a new IP4 Group:

Name: fwC-remotenets

Add fwA-net and fwB-net to the Group members

Click Ok

10. Firewall C – Pre-shared keys

Follow the instructions in step 2 to add a pre-shared key called fwABC-psk to firewall C. The passphrase has to be the same as the passphrase on firewall A.

11. Firewall C – IPsec interfaces

Go to Interfaces -> IPsec.

Add a new IPsec Tunnel.

In the General tab:

General:

Name: ipsectunnelCA

Local Network: lannet

Remote Network: fwC-remotenets

Remote Endpoint: fwA

Encapsulation Mode: Tunnel

Algorithms:

IKE Algorithms: High

IKE Life Time: 28800

IPsec Algorithms: High

IPsec Life Time: 3600

IPsec Life Time: 0

In the Authentication tab:

Authentication:

Enable Pre-Shared Key and select fwABC-psk from the dropdown list.

Click Ok.

12. Firewall C – Rules

Go to Rules -> IP Rules.

Create a new IP Rule Folder called lan_to_fwA.

In the new folder, add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: lan

Source Network: lannet

Destination Interface: ipsectunnelCA

Destination Network: fwC-remotenets

Click Ok.

Add a new IP Rule.

In the General tab:

General:

Name: allow_all

Action: Allow

Service: all_services

Address Filter:

Source Interface: ipsectunnelCA

Source Network: fwC-remotenets

Destination Interface: lan

Destination Network: lannet

Click Ok.

Save and activate the configuration on firewall C.